## Slide 1: Comparing SLAM Systems Across Sensor Modalities
Elias Bitsch, Philip Stix, Viktoriia Ovdiienko, Jiayi Zhou
Einsatz Autonomer Robotersysteme Lab, WS 2026/27
Notes: Group of four. Each member evaluated one SLAM system of their choice on the same dataset with the same metrics.

## Slide 2: Task and approach
1
Shared dataset
M3DGR ground robot, 3 indoor sequences with motion-capture ground truth
2
Own SLAM system
One per member, freely chosen, ideally a different sensor modality or paradigm each
3
Same metrics
ATE and RPE with evo, N runs per system, one central evaluation pipeline
Research question: how do SLAM systems with different sensor modalities compare in accuracy and robustness on the same ground robot, and which failure modes explain the differences?

## Slide 3: Dataset: M3DGR (IROS 2025)
Differential-drive ground robot
Sensors
  Livox MID-360 and Avia 3D LiDAR
  RealSense D435i RGB-D with IMU
  Wheel odometry (20 Hz)
Ground truth: OptiTrack motion capture
MIT license, ROS 1 bags, about 2 GB per sequence
Sequence | Difficulty | Challenge
Varying-illu01 | easy | nominal case
Dynamic01 | medium | moving people
Dark03 | hard | darkness
Hard cases are chosen so that each sensor modality fails differently: cameras need light, LiDAR needs geometry, odometry needs traction.

## Slide 4: Evaluated SLAM systems
Member | SLAM system | Sensors | Paradigm | Loop closure
Elias Bitsch | MASt3R-SLAM | monocular RGB | 3D foundation model, dense | yes
Philip Stix | [system] | [sensors] | [paradigm] | [yes/no]
Viktoriia Ovdiienko | [system] | [sensors] | [paradigm] | [yes/no]
Jiayi Zhou | [system] | [sensors] | [paradigm] | [yes/no]
All systems run with the authors' default parameters; only calibration and topic names are adapted.

## Slide 5: Evaluation methodology
Standard metrics only
  ATE: absolute trajectory error, RMSE (Sturm et al. 2012)
  RPE: relative pose error per metre (Sturm 2012, Kümmerle 2009)
  Robustness: success rate, tracked fraction
Umeyama alignment (Zhang and Scaramuzza 2018)
  SE(3) for metric systems
  Sim(3) for monocular systems, scale reported
Protocol
  N = 5 runs per system and sequence
  Median and IQR, failures reported
  Offline processing: every frame is used
Resources as context only
  CPU, RAM, GPU memory, runtime
  Always stated with the hardware

## Slide 6: Automated evaluation pipeline
Data
M3DGR sequences, ground truth in TUM format
Runners
one per system, any machine, container or ROS
Results
trajectory, map, resources and metadata per run
Evaluation
evaluate.py with evo: ATE, RPE, robustness
Figures
notebooks create the paper figures and tables
One command reproduces all figures from the raw results.
Every run stores the system version, parameters and hardware.

## Slide 7: Timeline
Lab 1
Dataset plays back, ground truth in TUM format, system chosen
Lab 2
Each runner produces a trajectory and a map for one sequence
Lab 3
All runs done, notebooks produce the figures
Lab 4
Full paper draft, discussion of failure modes
Final
Presentation, paper and repository submitted

## Slide 8: Results: trajectories
Key observations
  [observation 1]
  [observation 2]
  [observation 3]
[Trajectory overlay of all systems and ground truth]
paper/figures/trajectory_overlay.pdf

## Slide 9: Results: accuracy and robustness
System | Varying-illu01 | Dynamic01 | Dark03 | Success
MASt3R-SLAM | - | - | - | - / 15
[system 2] | - | - | - | - / 15
[system 3] | - | - | - | - / 15
[system 4] | - | - | - | - / 15
ATE RMSE in metres, median (IQR) over N = 5 runs. Generated by notebooks/02_trajectories.ipynb.

## Slide 10: Discussion and limitations
Failure modes and theory
  Monocular: scale is unobservable
  Darkness: visual features vanish
  Without loop closure: drift accumulates
  [findings per system]
Limitations
  Software-synchronised sensors, rolling shutter
  Default parameters only
  Small number of runs
  Different hardware per system

## Slide 11: Thank you
Questions? Code and results: github.com/eliasbitsch/bEARL